## Slide 1: Introduction to Robots and the Mind - Programming with Sensors -
Bert Wachsmuth & Michael Vigorito
Seton Hall University

## Slide 2: Last Time
Open vs Closed Loop controllers
  Controls a system using only the current state and its model of the system
  Has a feedback loop that measures differences between actual and desired state and takes corrective action if necessary
Active vs passive sensors
  Modify their environment and measure results
  Record some parameters of their environment

## Slide 3: EV3 Sensors
EV3TouchSensor
  getTouchMode() – registers touch
EV3ColorSensor
  getColorIDMode() – measures one of 8 colors
  getRedMode() – measure mount of reflected red light
  getAmbientMode() – measures the ambient light intensity
  setFloodlight(int colorID) – turn LED on in given color
EV3UltrasonicSensor
  getDistanceMode() – returns distance in meter
  getListenMode() – listens to other active ultrasound sensors
EV3GyroSensor
  getAngleMode() – measures orientation in degree
  getRateMode() – measures rotational velocity
  getAngleAndRateMode() – measures both direction and velocity

## Slide 4: Sensor Framework
For each sensor you want to use:
Define field of type “EV3 sensor name”
Define field of type SensorProvider and initialize to the desired sensor mode
Define field of type float[] to store the data measured by sensor
Define a method to query the sensor and return the sensor data in appropriate type

## Slide 5: Example
public static EV3UltrasonicSensor distanceSensor =
new EV3UltrasonicSensor(SensorPort.S1);
public static SampleProvider distanceProvider =
distanceSensor.getDistanceMode();
public static float[] distanceSample =
new float[distanceProvider.sampleSize()];
public static double getDistance()
{
distanceProvider.fetchSample(distanceSample, 0);
return distanceSample[0];
}

## Slide 6: Using the Sensor
If you follow the recommended sensor framework, it is easy to use a sensor:
public static void main(String[] args)
{
System.out.println(“D = “ + getDistance());
Button.ENTER.waitForPressAndRelease();
}

## Slide 7: Loops
Usually we want to query a sensor repeatedly: employ a while loop, which is deceptively simple:
while (condition_is_true)
{
// do this
}

## Slide 8: Distance Measuring Tool
Assuming you created the standard framework for the distance sensor, create the following main method:
public static void main(String[] args)
{
while (Button.ENTER.isUp())
{
System.out.println(“D=“ + getDistance());
Delay.msDelay(500);
}
}

## Slide 9: Distance Measuring Tool v2
public static void main(String[] args)
{
while (Button.ENTER.isUp())
{
double dist = getDistance();
Sound.playTone((int)(1000*dist), 100);
System.out.println("d = " + dist);
}
}

## Slide 10: A Complete Program
Task: Create a robot that drives forward if possible, avoiding any obstacle.
Need to clarify: “avoiding any obstacle”
Create a robot that drives forward as long as there is no obstacle ahead. If there is an obstacle, it avoids it by turning 90 degrees clockwise

## Slide 11: A Complete Program (2)
Robot needs to have:
Two motors
One distance sensor
Robot needs to do:
Drive forward
Detect obstacle
Avoid obstacle

## Slide 12: A Complete Program (3)
public class Avoider
{ // fields (not shown)
// methods
public static void driveForward() {}
public static void avoidObstacle() {}
public static boolean obstacleDetected() {}
public static void main(String[] args)
{
while (Button.ENTER.isUp())
{
driveForward();
if (obstacleDetected())
{
avoidObstacle();
}
}
}
}

## Slide 13: Making Decisions: if
The if statement lets you selectively execute code only if a certain condition is true
Syntax:
if (condition_is_true)
{ // execute this code
}
Or
if (condition_is_true)
{ // execute this code
}
else
{ // execute this code
}

## Slide 14: A WallHugger Robot
Create a robot that drives parallel to a wall if possible. If there is an obstacle ahead, it turns 90 degrees away from the wall.