## Slide 1: Robotics and EVT - line follower -
Bert Wachsmuth
Math and Computer Science
Seton Hall University

## Slide 2: Task: Follow the Yellow Brick Road
Suppose you have a differential drive robot with a light sensor in front, facing down.
Put the robot on a black line on white background and program it to follow that line indefinitely.

## Slide 3: Task: Follow the Yellow Brick Road
Assume: start on “gray” between, with black on the left, white on the right!!
  if (solid black)
  curve right
  else if (gray)
  go straight
  else if (white)
  curve left

## Slide 4: PID Controller
Proportional-Integral-Derivative controller: most commonly used feedback controller (closed loop)
  Proportional value P determines the reaction to the current error.
    P depends on the present error
  Integral value I determines the reaction based on the sum of recent errors.
    I depends on the accumulation (sum) of past errors
  Derivative value D determines the reaction based on the rate at which the error has been changing.
    D is a prediction of future errors based on current rate of change
    Change your Line-Follower algorithm to a proportional algorithm