## Slide 1: Robotics and EV3 - Behavior-Based Robots -
Bert Wachsmuth
Math and Computer Science
Seton Hall University

## Slide 2: Behaviors and Arbitrator
Drive drive = new Drive();
Bounce bounce = new Bounce();
Attack attack = new Attack();
Behavior[] behaviors = { drive, attack, bounce };
Arbitrator arbitrator = new Arbitrator(behaviors);
arbitrator.go();

## Slide 3: Behaviors and Arbitrator
Arbitrator starts a new thread (independend strand of execution)
That thread checks each behavior, starting with highest priority:
  wanna have control?
If yes, then
  suspend all lower behaviors
  start the action of the current behavior

## Slide 4: Behaviors and Arbitrator
2 threads are running simultaneously:
Arbitrator
  keeps checking which behavior wants control
Action method of active behavior
  Keeps running its action code

## Slide 5: Behaviors and Arbitrator
Arbitrator
  keeps checking which behavior wants control
Action method of active behavior
  Keeps running its “action” code
PROBLEM
Arbitrator determined that another behavior wants control
Calls ‘suspend’ of the active behavior and starts action method of new behavior
BUT the old action method is not done, while the new action method starts
Both can access a motor => Internal conflict

## Slide 6: What to do
We must make sure that the action method is done and stops executing as soon as its suspend method is called
Introduce extra boolean variable “suspended”
Set that variable to false when the action method starts
Ensure that the action method continuously checks “suspended” and finishes as soon as it is true
The suspend method simply sets “suspended” to true, which will automatically terminate the action method

## Slide 7: Questions
Why does the highest priority behavior not need a suspend method?
Why should you implement the suspend method of the highest priority anyway?
Why does the robot not resume normal drive after its attack behavior is triggered, but it does stop if the bounce method is triggered?
How could I stop the attack behavior as soon as no close object is detected any longer?
How could I “scan” for other nearby obstacles to attack?