## Slide 1: Robotics and EV3 - Behavior-Based Robots -
Bert Wachsmuth
Math and Computer Science
Seton Hall University

## Slide 2: Classical Robotics
Internal Representation of real world
Lots of state variables
Elaborate algorithms for decision making
Requires a lot of memory
Can be slow in reacting to sensor input
Requires outside intelligence, planning, and foresight

## Slide 3: Behavior-Based Robotics
Based on work in the 1980s at MIT by Professor Rodney Brooks:"Planning is just a way of avoiding figuring out what to do next“
Decompose problem into many “simple” behaviors
Strategy taken from the insect world:
  Insects have very little memory
  They do not remember things from the past
  They can not be trained easily (not Pavlov’s dog)
  Rely on sets of simple behavior
  Behavior rules are hard-wired (not learned)
  Many simple behaviors can work together to appear complex

## Slide 4: Behavior-Based Robotics
Firefighting robot behaviors:
Seek heat – if temperature differential is detected, move towards areas of increased temperature
Extinguish flames – if open flame is detected, spray CO2
Avoid damage – if heat is above 300 degrees, move away
Remain alive – if power source drops below certain level return to base and recharge

## Slide 5: Behavior-Based Robotics
Behavior is associated with a condition, an action, and a priority:
Behavior | Condition | Action | Priority
Seek heat | temperature differential detected | move towards increased temperature | low
Extinguish flames | open flame detected | spray CO2 | medium
Avoid damage | heat above 300 degrees | move away | high
Remain alive | power source drops below certain level | return to base and recharge | highest

## Slide 6: Subsumption Architecture
Decompose complex behavior into smaller, simpler behaviors
Establish conditions when each simple behavior kicks in
Establish priorities in case two behaviors want to act simultaneously (only one behavior is allowed at each time)
Define points of suppression to stop a behavior if another wants to take over
Use an arbitrator to manage behaviors and to decide whose turn it is

## Slide 7: Subsumption Architecture
Touch Sensor
Ultrasonic Sensor
Temperat. Sensor
Light Sensor
Collision reaction
Avoid obstacles
Spray CO2
Drive towards light
Motors
Fire Extinguisher
= Point of Suppression

## Slide 8: LeJOS Subsumption Architecture
LeJOS supports behavior-based robots by using a framework with two basic components:
Behavior
  Defines a single behavior, when it kicks off, and what should be done to suppress it
Arbitrator
  Decides which behavior should act based on priority and the triggers for individual behaviors

## Slide 9: LeJOS Subsumption Architecture
Behavior
  Method takeControl to decide when this behavior should kick in
  Method action to define what should happen while this behavior is active
  Method supress to define what to do when this behavior is being supressed
Arbitrator
  Defines an array of possible behaviors, sorted by priority
  A start method to start the arbitration process

## Slide 10: Defining a Behavior
Each behavior is defined in a separate class file (no main method), such as:
  import lejos.subsumption.*;
  public class BehaviorDrive implements Behavior
  {
  public void action() // what to do
  {}
  public void suppress() // how to stop doing it
  {}
  public boolean takeControl() // when to start doing it
  {
  return false;
  }
  }

## Slide 11: Defining the Arbitrator
import lejos.subsumption.*;
public class BehaviorRobot
{
public static void main(String args[])
{
Behavior drive = new BehaviorDrive();
Behavior collision = new BehaviorCollision();
Behavior attack = new BehaviorAttack();
Behavior behaviors[] = { drive, attack, collision };
Arbitrator arbitrator = new Arbitrator(behaviors);
arbitrator.start();
}
}

## Slide 12: Yielding to the Arbitrator
The arbitrator checks on the behaviors in order of their priority, where the priority is defined by the position in the Behavior array. For example, if:
Behavior behaviors[] = { drive, attack, collision };
Then drive has lowest priority (is checked last) while collision has highest priority (is checked first).
A behavior should not hog computing cycles so that the arbitrator has time to check whether another behavior should kick in.